## Slide 1: Network Monitoring & Deep Packet Inspection
Wissam Mallouli
wissam.mallouli@gmail.com

## Slide 2: Personal Background
Expertise in
  Formal methods
  Protocol design & engineering
  Monitoring techniques
  Evaluation and optimization
Working on several European research projects
Still coding from time to time (between us)

## Slide 3: Protocol development lifecycle
Vérification
Conception
formelle
Expression
des besoins
Implantation
Test de conformité
Conception
- préliminaire
- détaillée
Test de fonctionnement
- test d'intégration
- test unitaire …
Génération
automatique du code
Génération
automatique des tests
de conformité

## Slide 4: Ingénierie des protocoles
Les différentes étapes du cycle de vie des protocoles
  Expression des besoins
  Conception
  Description Formelle développement
  Vérification
  Implantation
  Test et validation
  Déploiement
  Maintenance

## Slide 5: Seminar plan
Network monitoring
  Needs for network monitoring
  Measurements (what, where and how)
  Limitations (briefly)
Deep Packet Inspection
  What is DPI and why it is needed
  Application classification
  Traffic attributes extraction
Security monitoring with DPI
  Abstract description
  Challenges
  Security properties

## Slide 6: Need for network monitoring Understand / Plan
3.5 billion mobile broadband users by 2015
Traffic increase 30 times (wrt 2010)
Understanding
  the drivers of this growth
  applications/usages
   contribute for a successful network planning
Need to have a clear visibility over the network
Status, traffic trends, peak time, evolution, etc.
Aggressive pricing the week-end/night

## Slide 7: Need for network monitoring Diagnose & react
Typical problem
  Remote user arrives at regional office and experiences slow or no response from corporate web server
Where to begin?
  Where is the problem?
  What is the problem?
  What is the solution?
Without proper network monitoring, these questions are difficult to answer
Corp Network
Regional Offices
WWW Servers
Remote User

## Slide 8: Need for network monitoring Diagnose & react
Typical problem
  Remote user arrives at regional office and experiences slow or no response from corporate web server
Where to begin?
  Where is the problem?
  What is the problem?
  What is the solution?
Without proper network monitoring, these questions are difficult to answer
Corp Network
Regional Offices
WWW Servers
Remote User

## Slide 9: Need for network monitoring Problems might still occur!
The Amazon Web Services Outage (April 2011)
Elastic Block Store: storage database for Amazon’s EC2.
  EBS clusters (Database nodes)
  Control Plane Services (accepts user requests and directs them to appropriate EBS clusters)
  Inter node communication on high bandwidth network and a lower capacity network as a back-up.
Manual Error with routine Network Upgrade Procedure (traffic directed to the low capacity network)
  many nodes were isolated.
  Etc. (for more info follow the link below)
Tens of sites and businesses impacted for 3 long days
(Source) http://aws.amazon.com/message/65648/

## Slide 10: What is network monitoring
Can be used to
  Understand the behavior of the network
  Detect faults and abnormal operation
  Network planning & resource optimization
  Network security (Intrusion & Attack Detection)
  Performance, quality & SLA monitoring
  CRM, Marketing
Sit above traffic measurements
  Gather traffic measures and performance indicators
  Analyze and correlate the measures in order to make a diagnosis
Process of observing or inspecting the network at different points
With the objective of
  Drawing operation baselines
  Produce reports
  Notify on abnormal operation
  Provide input to network management
Notes: To be able to optimize the available bandwidth
  59% of institutions do not monitor or manage bandwidth at all (Belcher, 2005)

## Slide 11: Network monitoring: Basics
Monitoring application
Interface for real-time monitoring.
Gathers, aggregates and correlates collected measures
Measurement unit
This performs the measurements
Performance analysis unit
This is where the measurements will be performed.
Observation points
Store collected data in a database for post analysis (trends, history, reporting …).
Calculate indicators (QoS parameters, KPIs).
Collects the required information for analysis.
The more observation points we have, the more accurate data we get.

## Slide 12: Network monitoring: Basics

## Slide 13: Seminar plan
Network monitoring
  Needs for network monitoring
  Measurements (what, where and how)
  Limitations (briefly)
Deep Packet Inspection
  What is DPI and why it is needed
  Application classification
  Traffic attributes extraction
Security monitoring with DPI
  Abstract description
  Challenges
  Security properties

## Slide 14: Complexity of network measurements
Size, complexity and diversity of the networks
  understand cause-effect relationships is difficult
Measurement is not an objective!
  meaningless without careful analysis
  Analysis depends on the monitoring objective
  Need to define
    What, where, how to measure?

## Slide 15: Determining What to Measure
Before any measurements can take place one must determine what to measure
Definition of metrics is closely related to the monitoring objective
There are many commonly used network performance metrics
  CAIDA Metrics Working Group (www.caida.org)
  IETF’s IP Performance Metrics (IPPM) Working Group

## Slide 16: Determining What to Measure
Example: Performance metrics can be classified into
  Network metrics
    Latency
    Throughput
    Arrival rate
    Link utilization, bandwidth
    Loss rate
  Application metrics
    Response time
    Connection setup time
    availability
  User quality metrics (depends on the application)
    Mean opinion score (VoIP)
    Quality of experience (Video – through estimation)

## Slide 17: Determining How to Measure
Active measurements
Passive measurements

## Slide 18: Determining How to Measure
Active measurements
  Send test traffic into the network
    Generate test packets periodically or on-demand
    Measure performance of test packets or responses
  Popular tools
    Ping: RTT and loss
    Traceroute: path and RTT
  Problems:
    Impose extra traffic on network and distort its behavior in the process
    May impact the behavior of the network (self interfering)

## Slide 19: Determining How to Measure
Passive measurements
  Observing network traffic at the measurement point(s)
    Packet capture (wireshark)
    Flow-based measurement tools (routers)
    SNMP tools (mostly used)
  Perform analysis for various purposes
Used to perform various traffic usage/characterization analysis/intrusion detection
Problems
  LOTS of data!
  Privacy issues
  Performance issues (wire speed packet capture and analysis)

## Slide 20: Comparison of active/passive measurements
 | Active measurements | Passive measurements
Configuration | Multi-point | Single or multi-point
Data size | Small | Large
Network overhead | Additional traffic | - Device overhead - No overhead if splitter is used
Purpose | Delay, packet loss, availability | Throughput, traffic patterns, trends, & detection
CPU Requirement | Low to Moderate | High

## Slide 21: Determining Where to Measure
Single point measurements
  Provide partial view of the network

## Slide 22: Determining Where to Measure
End-to-end measurements
  Provide a view on the performance between the the end points

## Slide 23: Determining Where to Measure
Multi point measurements
  Provide a view on the performance in the different “monitored” segments of the network

## Slide 24: Seminar plan
Network monitoring
  Needs for network monitoring
  Measurements (what, where and how)
  Limitations (briefly)
Deep Packet Inspection
  What is DPI and why it is needed
  Application classification
  Traffic attributes extraction
Security monitoring with DPI
  Abstract description
  Challenges
  Security properties

## Slide 25: Limitation of measurements
For years, monitoring used primarily
  Global traffic measures provided by Simple Network Monitoring Protocol
  Traffic data provided by routers (netflow data)
These information are always of great interest
However, are they sufficient?

## Slide 26: Limitation of measurements
What if we need to know:
  Who’s using Skype, P2P, VoD, etc.?
  Most popular applications on the network
  Proportion of VoIP calls with bad quality
  Quality of experience for video streaming
New means for providing accurate traffic measures is required
  Deep Packet Inspection is a good candidate

## Slide 27: Seminar plan
Network monitoring
  Needs for network monitoring
  Measurements (what, where and how)
  Limitations (briefly)
Deep Packet Inspection
  What is DPI and why it is needed
  Application classification
  Traffic attributes extraction
Security monitoring with DPI
  Abstract description
  Challenges
  Security properties

## Slide 28: Deep Packet Inspection
What is DPI and why it is needed
Application classification
Traffic attributes extraction

## Slide 29: What is DPI
Technology consisting of digging deep into the packet header and payload to “inspect” encapsulated content
  Content may be spread over many packets
Ethernet
Internet Protocol (IP)
Transport Layer (TCP/UDP)
Email (SMTP, POP3, IMAP)
Web (HTTP/S)
Instant Messaging (IM)
Peer-to-Peer (P2P) Applications
L2
L3
L4
L5 – L7
Packet Payload / Application Layers
Packet Header Layers
Deep Packet Inspection

## Slide 30: Why to DPI
Network Visibility
  Understand how bandwidth is utilized
    What is the application mix
    Who is using what, where and when?
Traffic Management (Application Control)
  Block undesired traffic (spam, worms, etc.)
  Prioritize and shape traffic (limit P2P, QoS, QoE)
  Advanced policy enforcement
  Zero Facebook, OTT services, per application policy rules
Network management
  Advanced billing (abandoning the unlimited data plans)
  New pricing may appear soon (user defined preferred applications for free, fees applies for the rest of applications)
Security
  Understand network attacks
  Core component in next generation firewalls
Etc.

## Slide 31: Inside DPI
Group packets belonging to the same session
Application classification
  Detect application type (Skype, Bittorrent, etc.) or application family
  Considered as the core of DPI
Protocol decoding and attribute extraction
  Parse the packet structure (this depends on the protocol & application)
  Get protocol attributes (IP @, port numbers, …)
  Get session attributes
  Events and attributes may involve different packets
    Attached file of an email

## Slide 32: DPI Drivers
Bandwidth (market driver)
  High penetration rate for broadband
    At home: ADSL2+, VDSL2, FTTx
    Mobile: 3G+ and 4G
  Bandwidth per user is ramping up (fixed and mobile)
Legal Interception (legislation driver)
  Requirement for service providers
  DPI is a core component
More Bandwidth
More Applications

## Slide 33: Market drivers: Applications
Video
Expected to reach 60% of mobile traffic
Continue to be highly popular (~ 40-60% BW)
VoIP
Use encryption BitTorrent, eMule
Viable choice for providers (Warner Bros, Spotify)
Skype, GoogleTalk, Yahoo!Voice, Facebook?
Serious competitor for traditional telephony!
P2P
Web video (Youtube, daily motion, video channel) + Telcos (IPTV & VoD)
Gaming
Consoles & PC offer “over the network” gaming experience
Stringent Bandwidth & Latency requirements
Social
Increasing traffic with diverse media contents (embedded video)
High signalling overhead (short frequent sessions)

## Slide 34: Seminar plan
Network monitoring
  Needs for network monitoring
  Measurements (what, where and how)
  Limitations (briefly)
Deep Packet Inspection
  What is DPI and why it is needed
  Application classification
  Traffic attributes extraction
Security monitoring with DPI
  Abstract description
  Challenges
  Security properties

## Slide 35: Application classification: the challenge
High number of applications and protocols
  Same Application – Different Implementations/versions
    Bittorrent has more than 30 different client implementations
    IM or VoIP don’t use similar protocols
  Evolving Architectures
    Client/server, Cashes, P2P, Client’s network surroundings: Firewall/NAT, Proxy
  Various Clients: PC, Smartphone, Gaming Console
  Symmetric vs. Asymmetric
Frequent Updates
  Can vary from every year to every month
  Typically will affect protocol format
Use of Encryption (Obfuscation)
  Primarily designed for counter measuring operator’s throttling and monitoring efforts (eMule, Bittorrent)
  In some cases protect proprietary implementation (Skype)
Need to differentiate use
  “Good” (legit streaming, SW updates) vs. “Bad” (pirated file sharing) P2P
Need to recognize application subtleties for proper actions
  Example: MSN IM – block VoIP & Streaming, allow Chat

## Slide 36: Application classification: Techniques
Classification techniques
  Port based classification
  Pattern matching based classification
  Statistical classification

## Slide 37: Application classification Evaluation criteria
Completeness
  Ratio of the application detection count over the expected detection count
  Low detection completeness indicates many false negatives.
  A false negative is the inability to classify a flow of application A as a flow of application A.
Accuracy
  Ratio of the correct detections over the detection count
  Measures how correct the detection technique is
  It may not be more than 100%.
  The lack of accuracy leads to false positives
  A false positive is the classification of application B as being application A.
Impacted if the classification technique is weak
Target: reduce false positives and false negatives in order to reach a sufficient enough accuracy

## Slide 38: Analysis by Port Numbers
Reasoning:
  Many applications and protocols have assigned port numbers (and widely used)
  Example: email
    Incoming POP3: 110 (995 if using SSL)
    Outgoing SMTP: 25
The Good - It’s easy  The Bad - It’s too easy 
  Many applications disguise the traffic using ports usually used by different protocols (80, 25, 110, …)
    Firewall and Nat traversal
  New or unknown protocols
  Applications that choose a random port number
  Accuracy ~ 30 – 70 % (close to 0% for some applications: P2P)

## Slide 39: Analysis by Port Numbers
Basic header information (port numbers)

## Slide 40: Analysis by Pattern Matching
Reasoning:
  Many applications have pure textual identifiers
    Defined in the application or protocol specification documents (RFCs, 3GPP, ITU)
    Ex: HTTP request must start with
    “Method URI HTTP/1.1”
Easy to search for
  Very easy if in a specific location within a packet
Uniqueness not always guaranteed
  Risk to have false positives!
Pattern may involve different packets
  Track the connection state and signature matching

## Slide 41: Analysis by Pattern Matching
information regarding connection state
Signature over several packets found

## Slide 42: Analysis by Pattern Matching

## Slide 43: Behavior and statistical analysis
Many protocols have statistical and behavioral “signatures” that are not related to the data contents:
  Packet size
  Inter-arrival delay
  Specific exchange that can be assimilated to a state machine
The detection requires a number of packets
Example
  Very close inter-arrival delays with low deviation from the average (VoIP)
Extremely effective analysis when application uses encryption or obfuscation
  Or simply when access to the payload is not possible
  Classification in the dark

## Slide 44: Behavior and statistical analysis
18 byte message
11 byte message
23 byte message
Either 18, 51 or 53 byte message
Client
Server
UDP Messages
Skype (Old Version) connection setup

## Slide 45: Packet classification: an expensive operation
High memory and processing requirements
  Will increase with the number of supported protocols and applications
Requires dedicated high capability hardware
  Multi-core technology
  Line rate packet capture capabilities
How it can be optimized???

## Slide 46: Packet Classification: Optimization perspectives (1)
Observation: traffic flows with the same server IP@ and port number will most probably have the same application type
Idea:
  Cache server identifiers (IP@ and port number) along with the application class/type
Work mostly for client/server based applications
  P2P traffic still needs to be classified
  Overall gain though
Preliminary evaluation shows a global gain of 30 ~ 60 % (vary with the application mix)
  Looks very promising
  Results to be confirmed on large scale evaluation

## Slide 47: Packet Classification: Optimization perspectives (2)
Observation: If a user is currently using an application, he will most probably use it again in the very near future
  Take yourself as examples 
Idea:
  Prioritize the classification by checking first the protocols and applications the user has recently used
    Require to maintain a cache per user (few items 5-10)
Why not to combine both ideas
  Cache of server identifiers and application types
  Per user cache of recently used applications

## Slide 48: Seminar plan
Network monitoring
  Needs for network monitoring
  Measurements (what, where and how)
  Limitations (briefly)
Deep Packet Inspection
  What is DPI and why it is needed
  Application classification
  Traffic attributes extraction
Security monitoring with DPI
  Abstract description
  Challenges
  Security properties

## Slide 49: From classification to attributes and events extraction
Application classification is a first step towards accurate traffic information extraction
  How can we get the HTTP method (Get, Post, etc.) if we don’t know the type of the traffic
  When the application type is known decoding becomes “easy”
What are traffic attributes?
  Protocol field derived from the packet data: IP@, attachment size, encoding type, etc.
  Flow parameter: packet mean size, inter-arrival delay, packets lost, reordered, etc.
  The application class can be considered as a traffic attribute

## Slide 50: Attribute extraction with DPI
With the extraction capability, DPI can provide input for other mechanisms as:
  Security analysis
  User quality analysis
Imagine the network as a database and DPI as an engine to extract data from this database!

## Slide 51: Network as a Database
Select user_id, perceived_quality Where (application = Video AND protocol = RTP)
Select flow_id Where (application = email AND attachment is executable)

## Slide 52: Seminar plan
Network monitoring
  Needs for network monitoring
  Measurements (what, where and how)
  Limitations (briefly)
Deep Packet Inspection
  What is DPI and why it is needed
  Application classification
  Traffic attributes extraction
Security monitoring with DPI
  Abstract description
  Challenges
  Security properties

## Slide 53: Security Monitoring with DPI
Abstract description
Challenges
Security properties

## Slide 54: The HBGary Hack
HBGary - experts in computer security
  computer forensics and malware analysis tools to enable the detection, isolation, and analysis of worms, viruses, and trojans
  implementing intrusion detection systems and secure networking
  performs vulnerability assessment and penetration testing of systems and software
  rootkit.com is a respected resource for discussion and analysis of rootkits
CEO Aaron Barr wanted to unmask Anonymous
  Those responsible for co-ordinating the group's actions, including the denial-of-service attacks that hit MasterCard, Visa, and others late last year
Anonymous response
  HBGary's servers were broken into, its e-mails pillaged and published to the world, its data destroyed, and its website defaced. As an added bonus, a second site owned and operated by Greg Hoglund, owner of HBGary, was taken offline and the user registration database published
(source) http://arstechnica.com/tech-policy/news/2011/02/anonymous-speaks-the-inside-story-of-the-hbgary-hack.ars/1

## Slide 55: The HBGary Hack
 | Attack Method | Attacked System | Vulnerability | Lost Assets
1 | SQL Injection | CMS on HBGary Federal's website, hbgaryfederal.com | CMS with missing validity check of SQL Parameters | usernames, e-mail @ & password hashes
2 | Password cracking using rainbow tables | Password hashes from 1 | Hashes without salt, weak passwords | clear text passwords
3 | Unauthorized use of passwords from 2 | E-mail, Twitter accounts, and LinkedIn accounts of HBGarry officials | Password double use | Email accounts of HBGary officials
4 | Unauthorized use of passwords from 2 | Machine running support.hbgary.com | Password double use | Non-superuser account of HBGary official
5 | Privilege escalation | Machine running support.hbgary.com | Privilege escalation vulnerability, system not up to date | Full access to HBGary's system, gigabytes of backups and research data
6 | Social engineering | Machine running rootkit.com |  | Integrity of rootkit.com

## Slide 56: The HBGary Hack: Where can security monitoring help?
 | Attack Method | Attacked System | Vulnerability | Lost Assets
1 | SQL Injection | CMS on HBGary Federal's website, hbgaryfederal.com | CMS with missing validity check of SQL Parameters | usernames, e-mail @ & password hashes
2 | Password cracking using rainbow tables | Password hashes from 1 | Hashes without salt, weak passwords | clear text passwords
3 | Unauthorized use of passwords from 2 | E-mail, Twitter accounts, and LinkedIn accounts of HBGarry officials | Password double use | Email accounts of HBGary officials
4 | Unauthorized use of passwords from 2 | Machine running support.hbgary.com | Password double use | Non-superuser account of HBGary official
5 | Privilege escalation | Machine running support.hbgary.com | Privilege escalation vulnerability, system not up to date | Full access to HBGary's system, gigabytes of backups and research data
6 | Social engineering | Machine running rootkit.com |  | Integrity of rootkit.com
SQL injection: In top ten most known vulnerabilities
(Top ten vulnerabilities are responsible for 60% of software bugs!)
Multi-lines security system: Is it possible to detect security attacks (SQL injection in this case) by inspecting the data encoded in inbound traffic?

## Slide 57: Security monitoring with DPI: Abstract description
The concept:
  Detect the occurrence of events on the network
    Input provided by DPI
    Event can be: packet arrival, HTTP POST request, etc.
  Inspect and analyze the succession of events to detect properties
    Property: Succession of events that are linked with “time” and “logical” constraints
      If we detect event “A”, then we MUST detect event “B” before 10 seconds
The idea:
  Monitor the network looking for the occurrence of properties.

## Slide 58: Security monitoring using DPI: Abstract description
Example: SQL injection
  www.abcd.com/page?name=Select * Where 1
  The events events:
    HTTP GET request
    URL parameter contains SQL statement
  The property
    It is not allowed to have a URL parameter containing SQL statement in an HTTP GET request
  If the property is detected on the network then most probably there is an attack attempt!
Nice Theory! But very challenging

## Slide 59: Security monitoring using DPI
Challenges
  The number of events that can occur on a network is huge!
    Solution: Use DPI for the events extraction
    Group events/attributes by application and add new ones when needed
  The expressivity of the properties (need to combine time and logical constraints)
  Complex analysis and processing especially in high bandwidth links
    Optimization techniques, multi-core implementations, smart traffic filtering

## Slide 60: Properties Expressivity
Considering security monitoring, properties can be used to express:
A Security rule describes the expected behavior of the application or protocol under-test.
  The non-respect of the Security property indicates an abnormal behavior.
  Set of properties specifying constraints on the message exchange
    i.e. the access to a specific service must always be preceded by an authentication phase
An Attack describes a malicious behavior whether it is an attack model, a vulnerability or a misbehavior.
  The respect of the Security property indicates the detection of an abnormal behavior that might indicate the occurrence of an attack.
  Set of properties referring to a vulnerability or to an attack
    A big number of requests from the same user in a limited period can be considered as a behavioral attack

## Slide 61: Properties Expressivity
A security property is composed of 2 parts:
  A Context
  A condition to verify
The “Context” and “condition” of a property are composed of:
  Simple events
    Conditions on attributes (IP @ equal to 1.2.3.4)
  Complex events linked by
    Logical operators (AND/OR/NOT)
    Chronological operator (AFTER/BEFORE)

## Slide 62: Properties Expressivity
A security property is composed of 2 parts:
  A Context
  A condition to verify
The “Context” and “condition” of a property are composed of:
  Simple events
    Conditions on attributes (IP @ equal to 1.2.3.4)
  Complex events linked by
    Logical operators (AND/OR/NOT)
    Chronological operator (AFTER/BEFORE)
If an HTTP Response is received (this is the context)
Then an HTTP request should have been received before (condition to verify)

## Slide 63: Security monitoring with DPI

## Slide 64: THANK YOU
Wissam Mallouli
wissam.mallouli@montimage.com

## Slide 65
shawez@jnu.ac.in
Lucie.poggi@agroparistech.fr
Mohamed-reda.belbahri@espci.fr
mariabargues1@gmail.com